## Slide 1
ring_gemm_M64N128K16_4slices 单算子性能表
metric
value
analytical_latency_cycles
1100
hardware_measured_cycles
1084
simulator_error_vs_measured(%)
1.48%
roofline_compute_utilization(%)
100.00%
analytical_compute_utilization(%)
23.27%
measured_compute_utilization(%)
25.00%
roofline_bandwidth_utilization(%)
81.25%
analytical_bandwidth_utilization(%)
18.91%
measured_bandwidth_utilization(%)
20.31%
Slide 1 · 单算子性能表

## Slide 2
ring_gemm 性能分析方法图
loop nest → template tile → load event → microtile timeline → final bounds
ring_gemm_bias.json Global: M=64, N=128, K=16 Local: A=64×4, B=16×32, Out=64×32
event规模 A events = 4 B events = 16
关键瓶颈 memory = 1100 ring = 612
最终延迟 latency = 1100
测量值
latency = 1024
根据 loop nest 生成events，再让 A/B/ring/PE/psum/writeback 在时间线上相互约束。
loop nest
template tiles
load events
microtile timeline
final bounds
Slide 2 · 总览

## Slide 3
Loop Nest 抽象模型：不同于通用算子，专用算子中的tensor tile会重复访问
for M_0 in range(2) for N_0 in range(1) for KM_0 in range(2) ag0(...) # A loads for KN_0 in range(4) ag1(...) ag2(...) # B loads ag4(...) # writeback
A load scope (M_0, N_0, KM_0) 2 × 1 × 2 = 4 events
B load scope (M_0, N_0, k_tile) 2 × 1 × 8 = 16 events
writeback scope output tile complete 2 write groups
抽象语义 • A 的event重复由 (M_0, N_0, KM_0) 决定 • B 的event重复由 (M_0, N_0, KN_0 / k_tile) 决定
• 这个 loop tree 导致请求个数不是由tensor footprint本身决定，而是会 request multiplicity
Slide 3 · loop scope 决定 event multiplicity

## Slide 4
Template Tile → Load Event：几何唯一块如何变成真实事件
footprint requests A=32 B=64 W=256
_split_requests_exact()
template tiles A=4, B=8, Out=2
_expand_ring_gemm_load_events()
load events A=4 B=16
A template tiles T0=(M[0:32],K[0:2]) T1=(M[0:32],K[2:4]) T2=(M[32:64],K[0:2]) T3=(M[32:64],K[2:4])
B template tiles 8 unique K-slices over N[0:32] each tile = 2×32 = 128B = 8 req 几何上只有 8 个 unique B tiles
event semantics A: 4 template tiles → 4 load events B: 8 template tiles → 16 load events 因此： b_requests=64 只是 footprint expanded_b_requests=128 才是执行真实请求流
Slide 4 · template tile 与 load event 是两个层次

## Slide 5
资源约束图：ping/pong、ring-ready、PE、psum 如何共同决定 coarse_start
A ping / pong
B ping / pong
psum ping / pong
A local ready
B ready
PE available
ring_ready = A ready + hop
psum slot ready
coarse_start = max(PE, ring, B, psum)
PE compute
当前实现里：A slot 要等最后一个 ring-hop 消费完才释放；B slot 在当前 coarse compute 后即可释放。
Slide 5 · coarse_start 由多资源依赖共同决定

## Slide 6
bank-level 简化模型：事件如何进入 memory timeline
当前已准确表达 • request 按 release_cycle 注入 • bank 内 row / phase 状态 • write buffer occupancy + forced drain • group ready = full-group completion • A/B/writeback event completion 反馈到上层 timeline
当前仍然简化 • ring_gemm 没完全复用 ordinary operator 的 controller / arbiter 语义 • bank 侧是 lighter event loop，不是显式 arbiter1 / arbiter2 竞赛 • 但它已经足够提供 A/B ready、writeback completion 和 memory_timeline 的关键路径
Slide 6 · 当前 memory model 的准确性与边界
A/B load event group (one event = many requests)
future_reads / future_writes
ready queues by bank
per-bank service (row / phase / drain)
group ready (full-group completion)
A event 0 8 requests release = 0 ready = 28
B event 0 8 requests release = 0 ready = 88
bank timeline 抽象过程 1. event 的 requests 先挂到 future_reads / future_writes 2. release_cycle 到了之后，按 bank_id 进入 ready queues 3. per-bank timeline 决定每条 request 何时完成 4. 只有当同一 group 的全部 requests 都完成时，才写 completion_by_group[group_key] 5. 这个完成时间就是 event ready time

## Slide 7
一个 output tile 内部：A/B event ready 与 coarse compute 时间
output tile 0 M[0:32], N[0:32]
1) A event
local-ready + ring-ready
2) B event
B local-ready
3) coarse compute
start / end
A event0
ring
ready
A event1
B0
ready 88
coarse k=0
start 88
end 104
B1
ready 104
coarse k=1
start 104
end 120
B2
ready 120
coarse k=2
start 120
end 136
B3
ready 136
coarse k=3
start 136
end 152
B4
ready 152
coarse k=4
start 152
end 168
B5
ready 168
coarse k=5
start 168
end 184
B6
ready 184
coarse k=6
start 184
end 200
B7
ready 200
coarse k=7
start 200
end 216
coarse 粒度：A(32×2) × B(2×32) 对一个 32×32 output tile 的单个 K-slice 做累加。A/B event 只负责给出 ready；coarse_start 才是 compute 真正开始的时间。
Slide 7 · A/B event ready 与 coarse compute 时间要分开看
local ready 28
local ready 44
ring
ready
ring
ready
ring
ready
ring
ready
ring
ready
ring ready 32
ring ready 108
ring ready 124
ring ready 48
ring ready 172
ring ready 192
final latency = max(compute_pipeline, ring, memory, AG)

## Slide 8
最终瓶颈选择：谁最后结束，谁决定 latency
compute 256
AG issue 256
ring 48
memory 1100
latency 1100
max(compute_pipeline, ring_timeline, memory_timeline, ag_issue) → 最晚结束者决定 latency
Slide 8 · final bound selection